## Slide 1: Doyle-Fuller-Newman (DFN) Full Order Model (FOM) Tutorial
UC Berkeley
eCAL
Professor Scott Moura
May 12, 2016

## Slide 2: Sample Output

## Slide 3: Background
This code is Matlab implementation of electrochemical model equations found in
Doyle, Marc, Thomas F. Fuller, and John Newman. "Modeling of galvanostatic charge and discharge of the lithium/polymer/insertion cell." Journal of the Electrochemical Society 140.6 (1993): 1526-1533.
Fuller, Thomas F., Marc Doyle, and John Newman. "Simulation and optimization of the dual lithium ion insertion cell." Journal of the Electrochemical Society 141.1 (1994): 1-10.
Thomas, Karen E., John Newman, and Robert M. Darling. "Mathematical modeling of lithium batteries." Advances in lithium-ion batteries. Springer US, 2002. 345-392.
and more…

## Slide 4: What it does
Simulates
  Terminal voltage [V]
  Solid & electrolyte concentrations [mol/m^3]
  Solid & electrolyte potentials [V]
  Internal temperature [K]
Generates
  Various static plots and animations
Takes as input
  An applied electric current time-series (time, current)
Requires
  A parameter file, which defines electrochemical model parameters
  OCP functions, electrolyte conductivity & diffusivity fcns
Assumes user is proficient with Matlab

## Slide 5: What it does NOT do
Provide polished user-interface. This code is for developers, and is under development.
Simulate
  Blended cathode materials
  Different particle sizes
  non Li-ion chemistries (e.g. NiMH)
  Battery pack geometries
  Mechanical stress
  Aging
Include the model identification code (PSO)
Some of these features are under-development
Keep your expectations reasonable please 

## Slide 6: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 7: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 8: Parameter File
Open params_NMC_Samsung_new_iteration.m
Embeds scalar parameter values
Generates a struct object p, which is passed throughout the code

## Slide 9: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 10: Open Circuit Potential Files
Open
refPotentialAnode.m
refPotentialCathode.m
Implements open circuit potentials for each electrode material
Computes OCP, and it’s derivative.

## Slide 11: Electrolyte Conductivity & Diffusivity
Open
electrolyteCond.m
electrolyteDe.m
Electrolyte conductivity & diffusivity are functions of local concentration
Computes conductivity/diffusivity and it’s derivative

## Slide 12: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 13: Input current files
All experimentally collected data is located in: data/Int_Obs/ directory
Samples:
1C Discharge
data/Int_Obs/1C_data_Oct_26_2015_05_sample.mat
5C Pulses
data/Int_Obs/dfn_5c.mat
UDDS drive cycle
data/Int_Obs/UDDS_data_Oct_26_2015_Sample_05sec.mat

## Slide 14: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 15: Main Script
Open dfn_scott_testing_Satadru.m
This is the main script that runs the DFN model
To input parameter file, go to line 19. Enter desired parameter file.

## Slide 16: Main Script
To load input current, go to line 33. Enter desired input current file.
To set initial voltage, go to line 138.

## Slide 17: Main Script
You are ready! Run the m-file.
The command window output will look like…

## Slide 18: Main Script
After running, the simulation outputs of interest are saved to struct object out. Go to line 467, uncomment, and save to a user-specified filename.

## Slide 19: Main Script – Ex: HEV Validation
To reproduce the model vs. experiment validation on the Samsung HEV cycle…
Use params_NMC_Samsung_new_iteration.m
Load data/Int_Obs/Samsung_HEV_data.mat cycle
Initialive model voltage to equal initial voltage from experimental data on line 138.
Run dfn_scott_testing_Satadru.m
The model will require 30min or so. After it’s finished, then the last code (line 507) will compute the RMS error between experiments and model

## Slide 20: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations

## Slide 21: Generate Plots and Animations
Open plot_dfn.m
Plot basic outputs: current, SOC, and voltage
Example: 1C discharge for 1000 sec

## Slide 22: Generate Plots and Animations
Open plot_dfn.m
Animate electrochemical states, e.g. solid & electrolyte concentrations and ionic current. Please feel free to uncomment/comment parts of code to view different echem states.

## Slide 23: Generate Plots and Animations
Open plot_dfn.m
Animate electrochemical states, e.g. solid & electrolyte concentrations and ionic current.
Example: Snapshot of 1C discharge animation

## Slide 24: Tutorial Outline
Parameter file
Material function files
Input current data
Main script to run DFN model
Generate plots and animations
Closing remarks: This code is under development. Future versions will have enhanced speed, accuracy, usability, etc. Enjoy!